MAPX.WK1, the Worksheet v2.0

                   A tool to find latitude and longitude
                   from a known reference on a map.  A
                   handy GPS companion.

                   Copyright 1995, John Ceccherelli


        ************************  WARNING  **************************
        * This program has been tested to the best of my ability,   *
        * but ...  If you plan to risk life, limb, or property on   *
        * this program, it's at YOUR OWN RISK. You are responsible  *
        * for its application and consequences.  The author is not  *
        * liable for damages arising from the use of this product.  *
        ************************  WARNING  **************************

        Quid Pro Quo:

        You get what you pay for and MAPX is free.  Free for personal
        and commercial use!  So feel free to copy, distribute, post, or
        purge as you wish.  Just make sure that this document accompanies
        the worksheet.  I would appreciate a note with your comments
        and a brief description of what you do with MAPX.


        Introduction:

        I've spent many late nights trying to figure out latitude and
        longitude of points on USGS Quadrangles.  It's a chore.  I've
        spent many dollars for rulers, overlays, and similar contraptions
        that never work all that well.  Conversely, I've been hiking
        deep in the backwoods with $500 of GPS satellite technology and
        have yet to find an easy way to translate positional coordinates
        back to the map.  This is why MAPX was written.  With a simple
        (and cheap) metric ruler, MAPX solves both problems.

        MAPX was developed to solve these problems with USGS 7.5'
        quadrangles.  It works well with scales down to 1/500,000 used
        for Sectional Aeronautical Charts.  Smaller than this and the
        results get dicey.  By the way, the bigger the denominator,
        the smaller the scale of the map.  For example, a USGS 7.5'
        quad has a scale of 1/24,000.  This is a larger number than
        1/10,000,000 - a scale you might find on a wall map of the USA.
        Remember: large scale-great detail, small scale-no detail.


        Rules:

        A few rules apply here.  First, North and West are positive (+),
        East and South are negative (-).  I live and travel north
        of the Equator and west of Greenwich so that's the way it is.
        (Ceccherelli's Convention).  This applies to latitude, longitude
        and the distances you will measure with your metric ruler.
        Notice I said METRIC ruler, no English distance units allowed
        because I'm a serious engineer (translation - the math is easier).
        Measurements from the metric ruler are entered as millimeters.
        Do not use MAPX for spans greater than 2 degrees from the
        reference, map scale errors will begin to be noticeable.  MAPX
        does not handle polar regions greater than +/- 88 degrees latitude.


        A Real Life Example:

        I recently went camping in the Catskills with some buddies of
        mine.  Due to scheduling constraints and minor commitments
        (like, my job), my friend Tom and I wouldn't be able to hit the
        trailhead until dark.  It would be a 3 mile hike, just me, Tom,
        and Coleman the lantern.  With a little luck and some expert
        navigation, we would meet the others on the south shore of Tunis
        Pond.  There was no room for error in this mission.  Rumor had
        it that beverages made from fermented grains were being served
        at the camp site.  The supply was sure to dwindle rapidly with
        each passing minute.  Time was critical, we had to execute
        flawlessly.

        There's a hitch though.  Tunis Pond is not on the trail.  It's
        a 300 meter bushwack north from a non-descript portion of the
        trail.  Fortunately, I'm equipped with a GPS receiver.  All we
        have to do is enter the lat and long of the point on the trail
        (waypoint) where we depart due north.  Dead reckoning 300 meters
        to the south shore of Tunis Pond should get us within shouting
        distance of the others.

        Tunis Pond is on Map 43 published by the New York-New Jersey
        Trail Conference.  These maps are OK except they have precious
        little positional information on them.  If you're lucky, there
        will be one latitude and longitude intersection labeled.  I'm
        lucky and this point is designated "the reference".

        Here's where MAPX comes in (finally).  First we have to enter
        the scale of the map.  This map is 1:63,360.

        So enter 63360 in cell B11

        The reference I'm using is 42ø 00' 00"  north latitude and
        74ø 30' 00" west longitude. Enter the lat øin B15, ' in C15 and
        " in D15.  Enter long øin B16, ' in C16 and " in D16.

        Now get out the metric ruler and measure the vertical distance
        from 42ø00'00' latitude.  Note it's vertical, the vertical component
        of the destination from the reference.  This will be a rectangular
        deal where we measure Y then X from the reference:

            Waypoint--> *            -
                                     |
                                     |<---vertical mm from x to * (27.5mm)
                                     |
                                     -            x <--Reference, 42ø00'N
                                                                  74ø30'W

        Enter 27.5 in B21 (it's positive because it's north of the reference)

        Next measure the horizontal distance:
           Waypoint--> *

                       |--horz distance = 80.5mm--|

                                                  x <--REF


        Enter 80.5 in B22 (it's positive because it's west of the reference)
        The worksheet should look like:

                  A           B      C     D     E      F          G
        1
        2                 MAPX, the Worksheet v2.0
        3                 ?1995  J. Ceccherelli
        4
        5  Note; Lat/long north of the Equator and west of Greenwich are (+
        6  south of the Equator and east of Greenwich are (-).  Distances
        7  are measured_FROM_the reference_TO_the target or waypoint.  West
        8  and north are (+), east and south are (-).
        9  ----------------------------------------------------------------
        10 Enter reference information in this section:
        11  Map Scale  1:   63360             Magnetic Dev:          14 W
        12
        13                    Deg   Min   Sec
        14                      ø    '     "                 Ellipsoid
        15   REF Latitude      42     0   0.0             a:  6378206.4
        16  REF Longitude      74    30   0.0           e^2: 0.00676865
        17 ----------------------------------------------------------------
        18 To find the Lat/Long of a point on the map (target), enter the
        19 X,Y distance to the target from the reference here:
        20 Distance, Ref to Target:
        21    VERTICAL mm    27.5
        22  HORIZONTAL mm    80.5
        23
        24                    Deg   Min   Sec
        25        Target:       ø    '     "        UTM Zone         18
        26       Latitude      42     0  56.5       Northing: 4651396.2
        27      longitude      74    33  41.7       Easting :    536301
        28 ----------------------------------------------------------------

        The waypoint latitude and longitude appear in row 26 and 27.
        Cool eh?  I plugged that data into my GPS receiver.  You also get
        the Universal Transverse Mercator coordinates; more on that later.

        We're hiking along wondering how much progress we've made
        toward that waypoint.  So I whip out the map and the GPS
        receiver.  A couple of minutes later, GPS tells me we're at
        41ø59'59"N lat, 74ø33'32"W long.  Great!?  Where's that on the
        map?  No big deal with MAPX, just enter 41ø59'59" and 74ø33'32"
        on lines 33 and 34.  Cells B37 and B38 give you the Y and X
        distance from the reference to the point on the map (where we
        are now).

                                                ref
                                                  x---
                      I'm here *                   ---  -0.5mm
                               |------ 77mm ------|



        I pencil in that point and see there should be a spring on
        my left... aaahhh, there it is.  Several gulps later, we continue
        on the trail knowing we're more than half way there.

        Well, we hit the waypoint with the aid of the GPS receiver.
        Switched over to geomagnetic mode (used a compass, GPS sucks
        for short distances), and dead reckoned due north 300 meters.
        We ended up at the south shore of Tunis Pond about 50 meters west
        of our friends!  The last drop of the aforementioned beverage had
        been consumed about 30 minutes prior to our arrival :-(.


        Polar Coordinates (Range/Bearing):

        The polar (azimuth and distance) coordinates from the reference
        to the position are also available in cells D37 and D38.  The
        azimuth is referenced to true north so north = 0ø, east = 90ø,
        south = 180ø, and west = 270ø (0ø and 360ø are both north).

        Chuck Hawley of West Marine, has described a very useful method
        to find your position on the map.  His "range/bearing" method
        is simple and all it requires is a protractor or plotter.
        Using a protractor with the example above, the position is 269.6
        degrees and 77 millimeters from the reference.  Some people find
        this measurement system easier than the X,Y rectangular system.
        Enter the map corner (or other convenient) latitude and longitude
        as a waypoint.  You then use the GPS range and bearing information
        to plot your position.  I find it is easiest to plot from the
        reference so you need to calculate the back azimuth (bearing)
        by adding or subtracting 180 degrees which ever is appropriate.
        Chuck suggests jotting down the distance conversion factor
        in the map margin.  The math is easy to do by hand and you
        don't need to bring a palmtop computer or similar device with
        you.  I find this method beautifully simple and elegant.

        If you are not comfortable with calculating in your head, I've
        included the Range/Bearing method in MAPX.
        The bearing from the reference to the waypoint is automatically
        displayed in cell D37.  The range in millimeters is in cell D38
        and the true ground distance is in cell D39.

        If you want to determine the range and bearing FROM the
        reference given the range and bearing TO the reference,
        use cells B46 and B47 for input.  The back azimuth from the
        reference is displayed in cells E46 and E47.  The X/Y
        coordinates are also displayed in cell G46 and G47.


        True to Magnetic Conversion:

        MAPX will also adjust for magnetic deviation.  Magnetic
        deviation for the local area is entered in cell G11.
        Following the rules, west deviation is (+) and east is (-).
        Cell H11 will automatically display E for east or W for west.
        If you forget the rules, cell H11 will remind you.  Input
        the true azimuth in cell B46 (range is not required).  Cell
        C46 will display the magnetic azimuth.


        Ellipsoid:

        The default ellipsoid supplied with the worksheet is Clarke
        1866.  This is the ellipsoid used for NAD27.  You can change
        it to WGS84 by entering a, 6,378,137 in cell G15 and e^2,
        0.00669438 in cell G16.  The Clarke 1866 values are a=
        6,378,204.4, e^2=0.006768658.  You can use any other reference
        ellipsoid to correspond with the datum of your map providing
        you can find the appropriate values for equatorial radius (a)
        and eccentricity squared (e^2).  See Appendix.


        Universal Transverse Mercator (UTM) Conversion

        MAPX converts lat/long to UTM!  You may have already noticed the
        UTM output for the target and waypoint.  If you want to convert
        any ol' latitude and longitude to UTM, use the last two sections
        of the worksheet.  Be certain you are using the right ellipsoid.
        I like using lat/long a whole lot more than UTM.  You need to keep
        track of which hemisphere you're in (northern or southern).
        Where lat/long can place you uniquely anywhere on the Earth with
        just two pieces of data, with UTM you need four:
        Hemisphere (north or south), zone (1 through 60), northing, and
        easting.  I've combined hemisphere and zone to boil it down to
        three pieces of data.  If zone is positive (+), you're in the
        northern hemisphere.  If zone is negative (-), you're in the land
        down under (southern hemisphere).

        UTM is great for aiming artillery but I don't find it all that
        useful for navigation.  Many people like it because they can draw
        in the UTM grid on USGS quads.  I find it to be a major pain in the
        ass.  The grid is usually skewed from true north (unless the central
        meridian for the zone is the edge of the map).  I prefer to use the
        lat/long fiducials that are spaced every 2.5' on a 7.5' quad.  You
        draw in four lines and you end up with 12 additional reference
        points on the quadrangle.


        Accuracy:

        How accurate is MAPX?  It depends on the map scale, map
        projection, printing errors, and humidity.  Humidity?  Yup,
        paper can expand and contract +/- 1% due to humidity.  And,
        it's not necessarily uniform across the sheet.  This error
        is twice that incurred by using a spherical model for the
        Earth Vs. an ellipsoid.

        You can compensate for humidity and printing error by calculating
        the map scale yourself.  I use the bar scale on the bottom
        margin of USGS quadrangles to do this along with digital
        calipers.  For example, spanning 4km of bar scale, I measure
        166mm or .166 meters. 4000 meters / .166 meters = a scale of
        24,096.  The published scale is 24,000.  So this map has
        0.4% error.  Enter 24096 instead of 24000 for scale (B11).

        The smaller the map scale, the more distortion you get from
        placing the curved Earth on a flat sheet.  This will introduce
        errors.  For large scale USGS Quads like 24,000 and 63,360 scales,
        you won't be able to measure the effect (well... maybe on
        63,360 scales).  Minimize the error by using the closest
        reference available.  This is usually the corners of the map,
        use the closest corner for the reference.  Note that there are
        "crosshairs" every 2.5' on 7.5' quads.  They are often very hard
        to pick out through the clutter but they are handy for drawing
        in supplimental grid lines (only 4!).  This is much easier than
        drawing in the UTM grid.  These crosshairs appear every 7.5' on
        USGS 1:100,000 scale maps also.  You can punch in the lat/long
        of the crosshairs and MAPX will tell you where to find them!

        After you adjust for all the above, you still have to deal with
        the fact that the mapped feature may be wrong.  National Map
        Accuracy Standards used by the USGS say that no more than 10%
        of well defined features will be off by more than 1/50 inch.
        What about not so well defined features?  What about the 10%
        allowed to be off by more than 1/50 inch (.5mm)?

        MAPX displays distances to .1mm precision from the reference.
        That translates to 2.4 meters on the ground.  A .3mm pencil point
        is a 7.2 meter circle on the ground (1:24,000 scale).  GPS
        with SA on has CEP of 100 meters.  That's a 8.4 mm circle on
        the map.  Don't get wrapped around the precision axle.


        Thanks:

        Thanks to Ron Harris for his suggestions and critique of MAPX
        computations.  Thanks to Chuck Hawley for the "Range/Bearing"
        method.  Special thanks to Tom Cowell for prodding me into
        camping/hiking/canoeing situations where navigation turned
        out to be a matter of life and death rather than an interesting
        intellectual exercise.


        References:

        Snyder, John P., "Map Projections - A Working Manual", USGS
        Professional Paper 1395, second printing, 1989.

        Bowditch,N., "American Practical Navigator", U.S. Navy Hydrographic
        Office, Washington D.C., 1966.

        Duffet-Smith,P., "Practical Astronomy with Your Calculator",
        third edition, Cambridge University Press, 1988.

        Clarke,B., "Aviator's Guide to GPS", Tab Books, McGraw-Hill, 1994.

        Moulton,F.,"An Introduction to Celestial Mechanics", Dover
        Publications, 1970, originally Macmillan Company, 1914.

        Greenhood,D., "Mapping", The University of Chicago Press, 1964.

        Robinson et al,"Elements of Cartography", fifth edition,
        John Wiley & Sons, 1978.

        Thompson, M.,"Maps for America", third edition, U.S. Department
        of the Interior, U.S. Printing Office, 1988.


        Revision History:

        Version 1.23 - Release  12/94

        Version 1.24 - Documentation typos corrected  12/94

        Version 1.30 - Fixed latitude display error occuring from 30' 1/95
                       to 59.99' south.

                     - Fixed X/Y sign error when crossing reference
                       and waypoint over the prime meridian.

                     - Fixed longitude modulus error when crossing
                       reference and waypoint over International
                       Date Line.

                     - Added user configurable ellipsiod.

                     - Added polar (range/bearing) input and output.

                     - Added true to magnetic heading conversion.

        Version 2.00 - Added UTM conversion 2/95


        Appendix:

        Some Official Ellipsoids -

        Name:                  a           e^2          Use:

        GRS80              6,378,137     .006694380     WGS84
        Clarke 1866        6,378,206.4   .006768658     NAD27, North America
        Clarke 1880        6,378,249.1   .006803627     Africa, France
        International 1924 6,378,388     .00672267      rest of world
        Austrailian 1965   6,378,160     .00669454      Austrailia
        Krasovsky 1940     6,378,245     .00669342      Soviet Union
        Airy 1830          6,377,563.4   .00667065      Great Britain
        Bessel 1841        6,377,397.2   .00667443      Central Europe
        Everest 1830       6,377,276.3   .00663788      India, So. Asia



        ******************************************************************
        *  Questions or comments?  Send them to me, John Ceccherelli on  *
        *  CompuServe, 71011.3424  Internet: 71011.3424@CompuServe.com   *
        *  February 1995 - Wappingers Falls, NY                          *
        ******************************************************************